## Slide 1: STM32WBA Workshop GPDMA

## Slide 2: Agenda
#
Overview
#
#
ADC+UART+TIM with LLI controlled GPDMA
#
Structure of example
Conclusion
Hands-on
Theory
#
What’s next

## Slide 3: DMA overview

## Slide 4: DMA overview
A new DMA module
  2 hardware instances
    GPDMA with symmetric configuration
  Dual port DMA with dedicated path to APB
  Integrated DMAMUX features
  Linked-list based programming
  Flexible intra-channel and inter-channel input/output control
  Run-time isolation features
Off-load CPU for data transfers from a memory-mapped source to a memory-mapped destination
Application benefit
Notes: Possiamo fare linked list programming – sequenza di differenti transfer, che e’ quello che dimostriamo in questo handson
Ovviamente lo scopo e’ quello di offlodare la cpu

## Slide 5: GPDMA integration
DMA1
DMA2
SRAM1
117Kb
SRAM2
16Kb
SRAM3
64Kb
AHB2
AHB1
FMC
FLASH
APB1
APB2
Periph
Mem
Periph
Mem
GPDMA1
GPDMA2
port1
port0
port0
port1
FLASH
SRAM1
SRAM2
SRAM3
OCTOSPI
FMC
BKSRAM
AHB1
AHB2
AHB4
OTFDEC
APB1
APB2
MPCBBx block-based MPC
MPCWMx water-mark
memory protection controller
TZ
TZ
STM32F4x9
STM32H563
Notes: Comparazione con F4
DMA1 nell’F4 era connesso a periferiche diverse vs DMA2
In H5 GPDMA1 e 2 possono interfacciarsi con le stesse periferiche
Port1 di solito e’ suggerita per le memorie
Port 0 suggerita per accedere alle periferiche
Dual DMA, managing requests in //. It is easy to split DMA configuration
Dual port managing in // transfers on the bus
Split between slow & fast

## Slide 6: GPDMA key features 1/2
Bidirectional AHB master port(s): GPDMA1/2: 2 ports
Memory-mapped data transfers from a source to a destination
  Peripheral-to-memory
  Memory-to-peripheral
  Memory-to-memory
  Peripheral-to-peripheral
Autonomous data transfers during Sleep mode
8 Concurrent DMA channels for each controller
Transfers arbitration is based on a 4-grade priority policy
  One reserved highest priority queue for time-sensitive traffic
  Three lower priority queues with weighted round robin allocation
Notes: Possiamo supportare diversi tipi di transfer mem/mem periph/mem mem/periph
Possiamo transferire in sleep mode in maniera autonoma
Possiamo avere 8 differenti transfer concorrenti avendo 8 canali
Abbiamo 2 controller con 8 channel vs 1 controller 16 channels in stm32u5
Abbiamo una lista di priorita’ – 4 livelli, l’ultimo e’ un real time priority che blocca ogni altro data transfer

## Slide 7: GPDMA key features 2/2
GPDMA data handling
  Byte-based reordering
  packing/unpacking
Linear addressing mode
  Fixed addressing (typically for peripheral data register)
  Contiguously-incremented addressing (typically for memory access)
  Blocks up to 64kB (16-bit BNDT)
2D addressing mode (ch6..7), additional
  Repeated block mode: programmable repeated block counter (11-bit BRC, up to 2k blocks)
  Programmable source/destination signed burst address offset (2x 14bit, up to +/-8kB)
      Non-contiguous incremented/decremented addressing after each burst
  Programmable source/destination signed block address offset (2x 17bit, up to +/-64kB)
      Non-contiguous incremented/decremented addressing after each block
  padding/truncation
  sign extension
  left / right alignment
Notes: Possiamo riordinare I buffer e riallineare I bytes, possiamo fare padding
Linear addressing supportato da tutti I canali– possimao rimpire parte della memoria
2 canali per controller supportano il 2D addressing mode ad esempio in grafica e audio viene utilizzato per fare sorting dei dati

## Slide 8: GPDMA linked-list register file
The GPDMA will use nodes for those registers
TR1 - Transfer register 1
TR2 - Transfer register 2
BR1 - Block register 1
SAR - Source address register
DAR - Destination address register
TR3 - Transfer register 3 ... SA & DA offsets incremet for 2D
BR2 - Block register 2 ... block repeated SA & DA offsets for 2D
LLR - Linker list register ... link to next LL node & update parameters In our case each linked list node will update this GPDMA registers after previous GPDMA node is finished. This is automatically reconfiguring the GPDMA channel.
Notes: Linked list mode
E; una struttura in memoria che contiene la struttura per il transfer
Nella structure abbiamo il linked list register che punta all item successivo

## Slide 9: DMA block diagram
GPDMA
Channel datapath and transfer input control
AHB slave interface
Channel 7
Channel1
Channel0
DMA global registers
DMA channel registers
Channel 7
Channel1
Channel0
Arbitration
Transfer output control
Data transfer generation
Link transfer generation
AHB master port 0
AHB master port 1
Interrupt generation
Event generation
Channel state management
Security and privilege management
Clock management
32-bi t
AHB
DMA requests
DMA triggers
DMA clock
Stop DMA channel
in debug mode
32-bit AHB
32-bit AHB
DMA channel interrupt
DMA channel xfer complete
DMA illegal event (vs. security)
DMA clock request
Notes: Abbiamo DMA request, trigger per triggherare I transfer, 8 channel slave ahb slave, master port
Contiene la security and priviledge menagment – alcuni canali DMA possono essere sicure e priviledge ad esempio per bloccare l’accesso ad alcune memorie/periferiche

## Slide 10: DMA specific implementation & user guidelines
Feature | GPDMA
Master port(s) | 2x (32-bit) AHB (*)
DMA transfers | Single and bursts
DMA scheduler | FIFO-based bursts (dual issue)
Number of channels | 8
Channel FIFO size | Ch0-3 (**): 8 bytes (2 words) Ch4-7 (***): 32 bytes (8 words)
Channel addressing mode | Ch0-5: linear Ch6-7: 2D addressing
Channel with peripheral early termination (I3C) | Ch0 and Ch7
Maximum request ID | 135
Maximum trigger ID | 43
    (*): GPDMA master ports:
      Port#0 should be typically allocated for transfers to/from peripherals
        There is a direct hardware datapath to APBx peripherals, out of the AHB matrix
        AHB1 peripherals are the default slave target of the AHB matrix
      Port#1 should be typically allocated for transfers to/from memory
        SRAM1 is the default slave
      In any case, any GPDMA target can be addressed from any port
    (**): These channels should be typically allocated for transfers from/to an APB/AHB peripheral and SRAM
    (***): These channels may be also used for transfers from/to a data-demanding AHB peripheral and SRAM, or for transfers from/to external memories
      4-word burst should be privileged when applicable for faster performances (faster back-to-back transfers, lower bus utilization)
Notes: Alcuni canali hanno una fifo piccola
Altri hanno una fifo piu grande
Possiamo assegnare ogni periferica ad ogni canale che vogliamo

## Slide 11: Structure of example

## Slide 12: ADC and UART with LLI controlled GPDMA transfer triggered by TIMER
  Use NUCLEO-WBA52 board and STM32CubeIDE
  Setup ADC to
    convert 4 channels in circle - channels 0, 2, 6, 13
    generate DMA requests
  Setup USART to
    transmit obtained data
  Setup TIM to
    generate a 1 second trigger
  Set GPDMA with linked list
    to get data from ADC and transfer them to buffer after trigger
    to get data from buffer and transfer them to UART3
Notes: Usiamo ADC1 per ocnvetire 4 canali in continua x una DMA request
Usiamo USART3 per plottare dati sul PC
TIM15 per fare il trigger
Useremo il linked list mode

## Slide 13: ADC + UART + TIM with LLI controlled GPDMA transfer
If ADC and UART work in loop without a trigger, it may cause a crash of terminal due to high baud rate.
We can slow down the GPDMA by adding trigger.
As trigger source in our case, we will use a timer TIM15 with period of 1s.
Then the GPDMA transfer will be conditioned by this trigger event.
Notes: Timer e’ usato per evitare che il terminale crashi e per far vedere la feature di trigger

## Slide 14: ADC + UART + TIM with LLI controlled GPDMA transfer
GPDMA ch
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
UART3
CH4
DR
CH1
CH2
…
CH4
64(BDTR)
GPDMA NODE 1
SRC - ADC
DST - MEM
64 - BDTR
Trg – TIM15
TIM 15
Notes: All’inizio dalla linked list facciamo il load della config 1
Attendiamo il trigger di tim 15 e trasferiamo I dati da ADC a memoria
Una volta che il transfer e’ finite, carichiamo il nodo 2 della linked list e iniziamo il transfer verso la usart3

## Slide 15: ADC + UART + TIM with LLI controlled GPDMA transfer
GPDMA ch
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
UART3
CH4
DR
CH1
CH2
…
CH4
64(BDTR)
GPDMA NODE 1
SRC - ADC
DST - MEM
64 - BDTR
Trg – TIM15
TIM 15

## Slide 16: ADC + UART + TIM with LLI controlled GPDMA transfer
GPDMA ch
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
UART3
CH4
DR
CH1
CH2
…
CH4
64(BDTR)
GPDMA NODE 1
SRC - ADC
DST - MEM
64 - BDTR
Trg – TIM15
Trigger
TIM 15

## Slide 17: ADC + UART + TIM with LLI controlled GPDMA transfer
GPDMA ch
ADC1
Destination memory
CH1
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
DR
63(BDTR)
CH1
Trg – TIM15
TIM 15

## Slide 18: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
CH1
CH2
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
DR
CH2
GPDMA ch
Trg – TIM15
TIM 15
62(BDTR)

## Slide 19: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
CH1
CH2
…
CH4
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
DR
CH4
GPDMA ch
Trg – TIM15
TIM 15
0(BDTR)

## Slide 20: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
CH1
CH2
…
CH4
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
DR
DR
GPDMA ch
None
TIM 15
64(BDTR)

## Slide 21: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
CH1
DR
CH1
CH2
…
CH4
GPDMA ch
None
TIM 15
63(BDTR)

## Slide 22: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
CH2
DR
CH1
CH2
…
CH4
GPDMA ch
None
TIM 15
62(BDTR)

## Slide 23: ADC + UART + TIM with LLI controlled GPDMA transfer
ADC1
Destination memory
GPDMA QUEUE
GPDMA NODE 1
SRC - ADC
DST - MEM
GPDMA NODE 2
64 - BDTR
SRC - MEM
DST - UART
64 - BDTR
UART3
CH4
DR
CH1
CH2
…
CH4
GPDMA ch
None
TIM 15
0(BDTR)

## Slide 24: Hands-on
Please open STM32CubeIDE

## Slide 25: Conclusion

## Slide 26: Conclusion
GPDMA implementation on WBA
GPDMA key features
Autonomous data manipulation with no CPU load
Standard request x Linked list based programing
Notes: /* USER CODE BEGIN 2 */
MX_YourQueueName_Config();
HAL_DMAEx_List_LinkQ(&handle_GPDMA1_Channel6, &YourQueueName);
ATOMIC_SET_BIT(huart3.Instance->CR3, USART_CR3_DMAT);
__HAL_UART_ENABLE(&huart3);
HAL_DMAEx_List_Start(&handle_GPDMA1_Channel6);
ADC1->CFGR |= ADC_CFGR_DMAEN;
HAL_ADC_Start(&hadc1);
HAL_TIM_Base_Start(&htim15);

## Slide 27: What’s next

## Slide 28: ADC + UART + TIM + 2D – LLI GPDMA